## Slide 1
تطوير تقانة تصنيع الألياف البازلتية واختباراتها وجدواها الاقتصادية
حسام غانم
أ. م. د. باسل صنوفة
-
قسم هندسة التصميم الميكانيكي
هندسة صناعية
نظراً لانتشار الصّخور البازلتيّة وبكميّاتٍ هائلةٍ جداً في الجمهوريّة العربيّة السوريّة ونتيجة الطّلب المتزايد عالميّاً على منتجاتها وذلك من خلال عمليّة صهرها في درجات حرارةٍ مرتفعةٍ تتراوح بين (1400-1650 C˚) لإنتاج الألياف البازلتيّة المستمرّة (BCF) التي تشكّل المادّة الأساسيّة للعديد من المنتجات البازلتيّة الأخرى اللاّحقة، مثل: (الخيوط والقضبان والأنابيب والأقمشة والملابس"البازلتيّة"، وغيرها الكثير)، جاء هذا البحث لدراسة إمكانيّة تطبيق استثمار الصّخور البازلتيّة في سورية- محافظة السّويداء- ودراسة الجدوى الاقتصاديّة لهذا الاستثمار، بالإضافة إلى دراسةٍ تصميميّة لآلة مقترحة لتصنيع الألياف البازلتية باستخدام تقانة الغزل بالطرد المركزي والعمل على نمذجتها ومحاكاتها باستخدام برنامج (Solid Works).
يُعدّ هذا البحث وبحسب معرفة الباحث من أوّل الأبحاثِ التي تَدرس خواص الألياف والخيوط البازلتيّة السوريّة المستمرّة سَعياً إلى تَحسين خَواصِها، بالإضافة إلى تصنيع بعضٍ من منتجاتها (الحبال البازلتيّة والمنسوجات البازلتيّة) لتحديد خواصها من خلال إجراء عدّة اختباراتٍ عليها، وتوصّل البحث إلى عدّة نتائج أهمّها:
إمكانيّة تطبيق هذا الاستثمار وبطاقةٍ إنتاجيّةٍ تبلغ 2500 طن سنوياً مبدئيّاً، وبربحٍ إجمالي سنوي يبلغ 2.393.350 $ US، وبفترة استردادٍ لرأس المال تبلغ 3.05 سنة.
إنتاجية الآلة المقترحة حوالي نصف طن من الألياف البازلتية في الساعة الواحدة.
تتمتّع الألياف والخيوط البازلتيّة بخواصٍ مُميّزةٍ ستجعلها في الوقتِ القريبِ مِن الموادِ الخام المطلوبةِ في السّوقِ العالميّةِ خاصّةً وأنّها بَاتت تُعتبرُ الحلّ الأمثل مقارنةً بالأليافِ الكربونيّةِ والزجاجيّةِ، وسيكون لها دور كبير في سورية خاصّةً في مرحلة إعادة الإعمار وذلك في حالِ تمّ استثمار الصّخور البازلتيّة المتوفّرة فيها بكميّاتٍ هائلةٍ تُقدّر بملياراتِ الأمتار المكعبة.
المُعالجة السّطحيّة للخيوط البازلتيّة بثاني أوكسيد الزيركونيوم (ZrO2) أدّى إلى زيادة مقاومتها للتآكل القلوي وتحسين قوّة شدّها.
تمّ قدر الإمكان توصيف اختبار الشد للحبال والمنسوجات البازلتيّة ليكون انطلاقة أوليّة لباقي الباحثين في هذا المجال كي يتمّ الاستفادة منه والعمل على تطويره.

## Slide 2
Developing the Technology of Manufacturing Basalt Fibers, their Tests and Economical Feasibility
Hossam Ghanem
Assistant Prof. D. Basel Sanoufeh
-
Department of Mechanical Design Engineering
Industrial Engineering
Due to the spread of basalt rocks in very large quantities in the Syrian Arab Republic and as a result of the increasing global demand for its products, through the process of melting it at high temperatures ranging between (1400-1650 C˚) to produce basalt continuous fibers (BCF), which constitute the basic material for many basalt products, other subsequent ones, such as: (“basalt” yarns, rods, tubes, fabrics and clothes, and many others), this research came to study the possibility of applying basalt rocks investment in Syria - Al-Swaida Governorate - and study the economic feasibility of this investment, in addition to a design study for a proposed machine for manufacturing basalt fibers using centrifugal spinning technology, and it was modeled and simulated using the (Solid Works) program.
This research is considered, according to the researcher's knowledge, one of the first studies that studies the properties of Syrian basalt continuous fibers and yarns in an effort to improve their properties, in addition to manufacturing some of their products (basalt ropes and basalt textiles) to determine their properties by conducting several tests on them. The research reached several results, the most important of which :
The applicability of this investment with a production capacity of 2,500 tons per year initially, with a total annual profit of 2.393.350 $ US, and a payback period of 3.05 years.
The productivity of the proposed machine is about half a ton of basalt fibers per hour.
Basalt fibers and yarns have distinctive properties that will soon make them raw materials required in the global market, especially since they are considered the ideal solution compared to carbon and glass fibers, and they will have a major role in Syria, especially in the reconstruction phase, if the available basalt rocks are invested it has huge quantities estimated at billions of cubic meters.
Surface treatment of basalt yarns with Zirconium Dioxide (ZrO2) has led to an increase in its resistance to Alkali Corrosion and an improvement in its tensile strength.
The tensile test for ropes and basalt textiles has been described as much as possible to be a preliminary start for the rest of the researchers in this field in order to benefit from it and work on developing it.